## Slide 1
NVIDIA SPARK HACK SERIES · SEATTLE · "SEE" TRACK
Chrono-Surge
Retained Surgical Item Detection — an offline visual second-check
Built on NVIDIA VSS (video-search-and-summarization) + Cosmos3 VLM

## Slide 2
PROBLEM STATEMENT
Retained surgical items are a preventable “never event”
› Sponges, needles, and instruments still get left inside patients.
Tracked by CMS/The Joint Commission as a “never event” — preventable, yet still happens under time pressure.
› Manual counting is the current safety net — and it's fragile.
Relies on a nurse/tech tallying items out loud during handoffs, fatigue, and shift changes. No independent check.
› Hardware fixes (RFID tags, barcoded sponges) require per-item retrofitting.
Added cost and workflow change for every single instrument and sponge in inventory.
› The gap: a passive, camera-only second-check that needs no new hardware.
Something that watches the existing tray setup and catches what a tired human count might miss.
Chrono-Surge

## Slide 3
THE SOLUTION
What Chrono-Surge does
› Watches a fixed camera view of the tray/sterile field.
No new sensors — just a camera pointed at the existing setup.
› Tracks every item's zone over time: TRAY → HANDS → FIELD → back.
A Vision-Language Model reports what it sees; Chrono-Surge tracks the trajectory.
› Flags HAZARD the moment an item enters the field and never returns.
The one transition that actually matters clinically — not just “item missing.”
› Live dashboard: Safety Monitor, Live Inventory, Telemetry, Audit trail.
Every run is persisted to disk — video, transcript, and summary.
SAFETY MONITOR
CRITICAL — RETAINED ITEM
“Gauze-Pack entered FIELD at 00:32 and did not return by end of clip.”
LIVE INVENTORY
Pencil-A
start 1 → end 1
Gauze-Pack
start 1 → end 0
ID-Card
start 1 → end 1
Chrono-Surge

## Slide 4
WHY HOSPITALS CARE
A safety net that fits into how ORs already work
› Retained items mean reoperation, patient harm, and malpractice exposure.
Direct cost and liability every time the manual count fails.
› Passive monitoring — doesn't slow the surgical team down.
No new counting ritual, no new tags to scan — it runs alongside existing protocol as a second check.
› Runs fully on local infrastructure — nothing leaves the building.
VLM inference happens on-prem via NVIDIA VSS; important for PHI/HIPAA-sensitive video.
› Low integration cost: one camera + existing VLM infra.
No per-instrument hardware retrofit, unlike RFID/barcode approaches.
Chrono-Surge

## Slide 5
APPROACH
From raw video to a trustworthy alert
1. Capture
Record (or simulate) tray-area video from a fixed camera.
2. Window
Split into short clips; auto-compress to fit the VLM's inline size cap.
3. Ask
Send each window to the VLM with a strict structured-JSON prompt.
4. Guard
Canonicalize names + reject hallucinated fragments before trusting counts.
5. Reconcile
Compare start vs. end state, window-to-window, to catch retained items.
6. Persist
Every run's evidence — video, transcript, summary — saved to disk.
Chrono-Surge

## Slide 6
ARCHITECTURE
Pipeline overview
Video Input
(upload / simulated)
ffmpeg
window + compress
Cosmos3 VLM
structured JSON
Guardrail Layer
canonicalize + reject
Continuity Check
ledger / baseline
Dashboard + Audit
Streamlit / analysis_runs/
Per-frame variant (standalone, not yet wired into the dashboard):
vss_adapter.py extracts frames → sends each as an image to Cosmos3 → cse.py's Chronological State Engine applies debouncing, occlusion tolerance, and the FIELD→ABSENT retention alert.
Kept separate from the live demo path to stay within VLM latency budget (~30–90s/call) for a real-time feel.
Chrono-Surge · see specs/system-design.md

## Slide 7
MODELS
VLM & LLM used
VLM — ACTIVE
nvidia/cosmos3-nano-reasoner
› Takes image or video + text prompt, returns structured object/zone JSON.
› Served locally via NVIDIA VSS “base” profile (OpenAI-compatible REST, port 30082).
› Every dashboard mode's detection call goes through this model.
LLM — DEPLOYED, UNUSED HERE
nvidia/nemotron-nano-9b-v2
› Text-only — cannot process images or video.
› Also part of the same VSS “base” profile deployment (port 30081).
› Not called by this pipeline — kept for completeness / future text-summarization use.
Chrono-Surge · all inference on-prem, no cloud round-trip

## Slide 8
GUARDRAILS
Preventing the VLM from hallucinating inventory
› Structured JSON contract, enforced by prompt.
The model must return an exact schema — no free-text answers get trusted directly.
› Name canonicalization — first-seen identity wins.
“Rectangular packet” later maps onto “packet” instead of becoming a phantom new item.
› Fragment rejection — stoplist + subset-duplicate filter.
Catches junk like a bare “white” or “thin” hallucinated alongside the real object name.
› Debounce + occlusion tolerance in the state engine.
A single noisy frame can never flip an item's official state or fire an alert alone.
REAL BUG WE CAUGHT & FIXED
A VLM response once produced:
“white label with text”, “white”, “text white with”
“metallic needle”, “metallic”
Three fragments of ONE object were about to become
three separate inventory rows.
Fix: the canonicalizer's match score was diluted by
dividing by the larger word set — a 1-word fragment
scored too low to merge. Fixed to score against the
smaller set, plus a stoplist as a last-resort filter.
Every drop is logged — nothing silently discarded.
Chrono-Surge · specs/inventory-guardrail-spec.md

## Slide 9
“SEE” TRACK FIT
Why this is a computer-vision story, not a checklist app
› The entire safety case rests on visual perception.
No sensors, no tags — the only signal is what a camera + VLM can actually see.
› Temporal visual reasoning, not single-frame classification.
Tracking an item's zone across time (TRAY→HANDS→FIELD→back) is a sequence-understanding problem.
› Hallucination-safe visual counting under real-world noise.
Handles occlusion, re-phrasing, and outright VLM hallucination — the hard edge of “seeing reliably.”
› A visual second-check for a high-stakes, real clinical workflow.
Demonstrates the “See” track's premise: vision models doing something a human easily misses.
Chrono-Surge

## Slide 10
LIVE DEMO
What we'll show
› 1. Mock Scenario gate-checks.
Round-trip (no alert), occlusion (no false alert), retention (exactly one HAZARD), endpoint drop (DEGRADED) — controlled validation of the dashboard's logic.
› 2. Live Analysis (10s windows) on a real tray video.
Watch the Safety Monitor update window-by-window, then flip to CRITICAL the moment an item enters the field and doesn't return.
› 3. Live Inventory in real time.
Object counts update per window, robust to the VLM re-wording the same object (“pencil” vs “yellow pencil”).
› 4. All-time stats surviving a mode switch / restart.
Sidebar token/latency totals are disk-backed — proof this isn't just in-memory demo state.
Chrono-Surge

## Slide 11
WRAP-UP
Known limitations & next steps
LIMITATIONS
› VLM latency (~30–90s/call) rules out true per-frame real-time analysis.
› Open-set object naming can still edge-case on very unusual phrasings.
› No live RTSP camera input yet — file upload / simulated video only.
NEXT STEPS
› Wire zone-tracking (TRAY/HANDS/FIELD) into the windowed live mode.
› Pilot against real recorded surgical-tray footage for validation.
› Add live RTSP input to move from file-upload demo to a real feed.
Chrono-Surge · Thank you